## Slide 1
WiFi-Sense
Contactless Human Presence Detection & Ambient Intelligence via Wi-Fi Electromagnetic Wave Fluctuations

## Slide 2
Sender ESP32 Node
Programmed to transmit continuous packet streams across 64 Wi-Fi channels. Functions as an RF signal emitter, creating an active electromagnetic field across the physical room.
Receiver-Manager Node
Receives transmitted packets across multi-channel spectra. Captures variations in received signal properties and streams raw metric data over the Serial port interface.
Hardware & Transceiver Architecture

## Slide 3
Serial Data Stream: Python interface continuously reads high-frequency packet telemetry from the Receiver ESP32 via Serial connection.
Automated File Logger: Structured Python script parses incoming stream metrics and appends clean numerical logs into dataset files.
Wave Perturbation Analysis: Captures physical electromagnetic scattering and absorption caused by obstacles and movement.
Data Acquisition Pipeline

## Slide 4
Empty Room
Baseline environment data with zero occupants. Represents natural background RF noise and static multipath baseline.
1 Person Present
Single human occupant in the space. Introduces distinctive signal attenuation and localized phase variance pattern.
2 People Present
Multiple occupants in monitored area. Creates compound electromagnetic reflection and dynamic interference matrix.
Occupancy Data Labeling

## Slide 5
XGBoost achieved peak classification score by effectively capturing non-linear gradient dynamics across all 64 Wi-Fi channels.
Machine Learning Performance

## Slide 6
Presence Accuracy
Reliable Camera-Free Sensing
By leveraging ensemble gradient boosting over multi-channel Wi-Fi signal power variance, WiFi-Sense accurately classifies room occupancy status with 86% accuracy without using any cameras, preserving complete user privacy.
Detection Accuracy

## Slide 7
Streamlit Real-Time Dashboard
3-Second Sliding Window
The Streamlit web dashboard visualizes incoming signal power across channels using a 3-second rolling window for live dynamic analysis.
Real-time metric windows are continuously streamed into the trained XGBoost model, rendering immediate occupancy predictions on screen.

## Slide 8
Heart Rate Sensing
Enhancing wave resolution to capture micro-disturbances caused by chest wall displacement and cardiac pulse cycles.
Elderly & Patient Care
Continuous non-invasive monitoring in hospitals and care facilities without requiring wearable body tags.
Automated Nurse Alarms
Triggering instantaneous emergency alerts to medical personnel if vital signs drop or critical anomalies occur.
Vital Signs & Healthcare Vision

## Slide 9
Building-Wide Scalability
Scaling transceiver node range to span entire multi-room floors, creating a seamless, non-intrusive security network with zero privacy tradeoffs.
3D Room Reconstruction
Utilizing high-precision multipath RF wave reflection mapping to reconstruct internal room geometry and simulate indoor spatial dynamics in 3D.
Smart Building & Privacy Security

## Slide 10
Questions & Discussion
Thank you for exploring the WiFi-Sense project.

## Slide 11
https://docs.espressif.com/projects/esp-hardware-design-guidelines/en/latest/esp32/_images/esp32-sche-core.png
Source: docs.espressif.com
https://cdn.prod.website-files.com/617960145ff34f911afe7243/692610a2df06ad0ee562a700_Analytics%20Dashboards%20with%20Real-Time%20Financial%20Data%20.jpg
Source: intrinio.com
Image Sources